## Slide 1: Analysis of PJM Interconnection Transition Cycle 1
Bill Louer
LinkedIn Profile
9/5/2024

## Slide 2: Outline
Introduction and Background
Objectives
Exploratory Data Analysis
Projects with Lowest Interconnection Cost
Conclusions
Appendix
Acknowledgements

## Slide 3: Introduction & Background
PJM transitioned from a serial to a cluster study approach.
PJM divided projects currently in the series queue into two clusters:
  Transition Cluster 1: AE1, AE2, AF1, AF2, AG1
  Transition Cluster 2: AG2, AH1
PJM analyzed the first cluster of projects (TC-1) and recently completed Phase 1 analysis.
This analysis addresses the TC-1 Projects that have just completed phase 1 analysis.

## Slide 4: PJM Transition to Cluster Study
Reference: PJM, Thomas, Jack; “Interconnection Process Reform”, April 27, 2022

## Slide 5: Objectives
Determine distribution of projects in the interconnection queue by:
  Technology
  MW Capacity
  Location
  Interconnecting Utility
Determine distribution of unit price of interconnection ($/kW).
Is there any correlation between interconnections costs and any of these factors?
Characterize the projects under some unit interconnection cost threshold.

## Slide 6: Exploratory Data Analysis

## Slide 7: Project Characterization (TC-1)
306 total projects in TC-1
Project technology type and MW capacity is primarily solar, storage, solar + storage.
3 Transmission Owners have the most projects applying to interconnect with their systems:
  ComEd
  Virginia E&PC
  AEP
Illinois, Virginia and Indiana dominate the project locations by total MW capacity.

## Slide 8: Project Distribution by Technology

## Slide 9: Project Distribution by State

## Slide 10: Plant MW Capacity by Resource
Natural gas, Transmission, and Offshore wind projects have median project capacities greater than 750 MW.
Wind, Solar, Storage have median project capacities of under 250MW.

## Slide 11: Interconnection Project Unit Cost Distribution ($/kW)
30 percentile: $ 90/kW
50 percentile: $ 170/kW
67 percentile: $ 310/kW
90 percentile: $ 573/kW
95 percentile: $ 728/kW

## Slide 12: Interconnection Unit Cost vs. Project Size
Unit Cost of Interconnection $/kW) is NOT well correlated to Project Capacity (MW)
However, projects over 1,000 MW (only 2% of TC-1 projects) generally have low unit cost of interconnection

## Slide 13: Distribution of Project Unit Interconnection Cost and Interconnection Voltages
The lowest median unit interconnection costs appear at 765kV and 345kV

## Slide 14: Distribution of Project Unit Interconnection Cost by Transmission Owner
Median unit costs are $300 /kW or less except for:
  Keystone Appalachian Transmission Company
  Mid-Atlantic Interstate Transmission Inc.
  PPL Electric Utilities
  American Municipal Power

## Slide 15: Projects with Lowest Interconnection Cost

## Slide 16: Projects with Low Cost of Interconnection
Generally, only 30% of projects which apply for interconnection proceed all the way through and sign an interconnection agreement.
Reasons may include:
  Project financing or problematic project economics
  Lack of or loss of developer funding
  Project delay or difficulty getting permits
  High Interconnection costs
It’s assumed that projects with low cost of interconnection are more likely to proceed than projects with high costs of interconnection.
Assuming true, what are the characteristics of the subset of projects in bottom 35 percentile of unit interconnection cost? ~ 100 projects

## Slide 17
Storage, Solar and Solar + Storage still represent the majority of projects by count and MW capacity.
American Electric Power, ComEd and Virginia all have the most MW capacity; but ranking has changed. AEP now first, followed by ComEd
A good percentage projects with AEP as the Transmission Owner are among the lowest 100 projects.
Indiana, Illinois, Virginia still have the most projects; but ranking has changed. (was Illinois, Virginia, then Indiana)
Project Characterization
Lowest 100 Unit Interconnect Cost

## Slide 18: Conclusions
PJM’s Transition Cycle 1 cluster of projects is comprised mostly of solar, energy storage and solar+ energy storage projects
Projects are primarily located in Virginia, Illinois and Indiana,
A high proportion of projects interconnect with ComEd, Virginia Electric Power Company and AEP
Unit Interconnection cost for projects have a median unit cost of $170/kW and 30% of projects have units costs of $90/kW or less.
A very high percentage of AEP’s projects are among the 100 projects having the lowest unit cost of interconnection.

## Slide 19: Appendix
Data Source: https://www.pjm.com/pub/planning/project-queues/Cluster-Reports/TC1/TC1_PH1_Executive_Summary.htm
Interconnection Process Reform: https://www.pjm.com/-/media/committees-groups/committees/mrc/2022/20220427/20220427-item-02a-interconnection-process-reform-presentation.ashx

## Slide 20: Acknowledgements
PJM makes data publicly available on their interconnection process.
This type of transparency is important for developers to understand the market.